## Slide 1
MFC · EXASCALE MULTIPHYSICS CFD
Reacting Flows & Combustion, on GPUs
Finite-rate H₂/O₂ chemistry, gas & condensed-phase detonations, and solid-fuel combustion — computed with the Multi-component Flow Code on NVIDIA A100s, from one source that runs on four CI-gated compilers.

## Slide 2
01
2D cellular detonation in Ar-diluted H₂/O₂
A piston-driven shock ignites 2H₂+O₂+7Ar and locks into a self-sustained Chapman–Jouguet detonation (~1600 m/s). Heavy argon dilution regularizes the transverse-wave pattern, so the classic cellular soot-foil structure is resolved directly on the mesh.

## Slide 3
02
3D detonation — cellular soot foil
The same case run in 3D on the four GPUs (millions of cells). Recording the peak pressure reached at every point traces the soot foil — the diamond fish-scale imprint of the detonation's transverse waves, forming here as the front sweeps down the channel. This diamond-cell pattern is the classic fingerprint of a detonation's cellular structure.

## Slide 4
03
Detonation diffracting around an obstacle
The detonation runs into a rotated-ellipse immersed boundary and wraps around it, staying vigorous (~3400 K). This surfaced a solver finding: CFL-adaptive time-stepping drives the timestep to NaN and silently hangs at the super-heated impact, while a fixed timestep sails through the diffraction.

## Slide 5
04
Condensed-phase detonation — a solid explosive
● NEW CAPABILITY
A programmed pressure burn converts reactant to product on the multi-fluid model (no ideal-gas chemistry): the two fluids share an EOS and differ only in reference energy, releasing heat through the mixture equation of state. A self-sustained ~7 km/s detonation forms — von Neumann spike, ZND reaction zone, Taylor rarefaction — bypassing the Cantera single-fluid lock.

## Slide 6
05
Burning solid-fuel grain
● NEW CAPABILITY
A solid cylinder injects H₂ off its surface into a hot O₂/Ar chamber; the fuel auto-ignites and anchors a surface diffusion flame (~2700 K). Enabled by two new immersed-boundary knobs — wall-normal blowing and injected-species — that let a solid surface transpire and inject fuel.

## Slide 7
06
Internal ballistics — pressure-coupled burn
● NEW CAPABILITY
A Vieille's-law burn rate (v ∝ pⁿ) turns the closed chamber into a feedback loop: combustion raises the pressure, which raises the burn rate, which raises the pressure — the defining signature of solid-rocket internal ballistics, reproduced from first-principles CFD.

## Slide 8
07
Hybrid-rocket fuel slab
A wall strip injects H₂ into a hot O₂/Ar crossflow, forming a boundary-layer diffusion flame (~2660 K) that lifts off the wall and burns downstream — the essential hybrid-rocket picture of fuel blowing off a surface into an oxidizer stream, at high resolution.

## Slide 9
08
Bluff-body flame holder
A fuel-injecting cylinder anchors a flame in its recirculating wake (~2630 K). The freestream carries no fuel, so combustion can only stabilize where the injected H₂ meets the oxidizer behind the body — the classic afterburner/ramjet flame-holder configuration.

## Slide 10
09
1D premixed propellant flame
A premixed H₂/O₂/Ar deflagration propagating at ~18.6 m/s with full multicomponent transport and finite-rate chemistry — the slow, diffusion-controlled counterpart to the shock-driven detonations.

## Slide 11
PERF
GPU performance
177× speedup
On a case-optimized 3D reacting run (H₂/O₂, 256k cells), a single A100 sustains 10.1 million cell-updates per second versus 57 thousand on one CPU core.
The same Fortran source runs on four CI-gated compilers (gfortran, nvfortran, Cray, Intel) and across CPU, OpenACC, and OpenMP-offload GPU back-ends.